## Slide 1: A proposal for research and development in the area of high energy sonoluminescence
hypersonic focused shockwaves

## Slide 2
Intense focused shock waves arguably have application in:
  research into ultra high temperature plasma physics
  production of nanophase materials
  “sonochemistry”
The common factor in each case is ultra high temperatures

## Slide 3: Implosions and temperature
"A Mach number is associated with every shock wave. This number represents the ratio of the shock wave to the ambient speed of sound. The temperature behind a shock wave is higher than that in front of it; the ratio of those temperatures is proportional to the square of the Mach number. For an imploding air bubble, the Mach number approaches infinity as the shock front moves closer to the focal point, which means that a tremendous amount of heating takes place. Furthermore, when the shock hits the center and explodes outward, the molecules that were behind the shock are suddenly in front of it again. The hot molecules are hit a second time, and their temperatures go up by another factor of the square of the Mach number.“
"Temperatures that can be reached by this mathematical model are therefore unimaginably high.“
Sound into Light Seth Putterman
Where vth = thermal velocity
kB = Boltzmann constant = 1.381x10-23 J/K
T = temperature (K)
m = mass of particle (kg)

## Slide 4
The downside of the imploding bubbles - Cavitation

## Slide 5
Cavitation

## Slide 6
Sonoluminescence means “light from sound.”
Sonoluminescence is normally studied within a small (~4 micron ambient radius) air bubble in a liquid such as water which has been exposed to variations in pressure from high frequency sound waves (typically ~30 kHz).
Making a virtue of necessity –
Sonoluminescence

## Slide 7
The supersonic collapse of the bubble launches an imploding spherical shock wave, the strength and velocity of which varies inversely as the square of the radius.
Thus if it were possible to focus the shock wave to a point (or a line), at zero radius its velocity and intensity would be infinite.
Limits on the minimum volume of the focus are imposed because imploding shock waves usually tend to become unstable as initial irregularities in sphericity become more significant at smaller scales.
Sonoluminescence - Mechanism

## Slide 8
Sonoluminescence

## Slide 9
Scientific American February 1995
Sonoluminescence

## Slide 10
Sonoluminescence - Bubbles “hotter than the Sun”

## Slide 11
“…Prospects for initiation of thermonuclear fusion reactions within a sonoluminescing bubble were suggested when theoretical simulations of the SBSL phenomenon by Wu and Roberts showed the existence of maximum bubble temperatures of the order of 10^8 K!”
“These extreme temperatures were limited to a small region of the bubble interior and were made possible by the launch of a shock wave within the already compressed gas. The shock focuses as it approaches the bubble centre and doubles its strength when reflected from the origin.”
“In an another study, Moss et al. showed that hydrodynamic simulations of a collapsing bubble containing D2 and D2O vapour provide the possibility for a small number of thermonuclear D–D fusion reactions in the bubble...”
Sonoluminescence and bubble fusion
Vijay H. Arakeri
Sonoluminescence - Bubbles “hotter than the Sun”
Department of Mechanical Engineering, Indian Institute of Science, Bangalore, India

## Slide 12: Implosion

## Slide 13
“The final 50 ps of the calculated collapse of an argon bubble. The bubble radius (outermost curve), shock wave location (inner curve), and emitting regions [optically thin (yellow), and optically [opaque] (black)] are shown. P is the relative emitted power (energy per unit time) of light in the visible part of the spectrum.” http://acoustics.org/pressroom/httpdocs/133rd/2apa10.html
Sonoluminescence implosion – output from a computer model
Bubble surface
Light emitting region (yellow)
Optically opaque (black)
Shock wave
1
2
3
4
5
LASNEX output

## Slide 14
arXiv:1303.4872 [physics.flu-dyn]
Bubbles within a gravitational field are not perfectly spherical. Sonoluminescence ideally should be carried out in microgravity

## Slide 15
Larger scale bubble -
Sonoluminescence rig
PHYSICAL REVIEW E 69, 066317 (2004)
Cavendish Laboratory, Cambridge
Excitation frequency = 20 - 200 Hz
Spin rate N ~ 20 rev./sec
Bubbles of 0.4 mm ambient radius (containing 23x10^14 xenon atoms) were excited by vibration at 35 Hz. Approximately 10^12 photons were emitted per collapse in the range 400–700 nm (over four orders of magnitude greater than the brightest SL reported previously), corresponding to a 1% efficiency of the conversion of mechanical energy into light.
Note bubble size two orders of magnitude larger diameter than for a conventional sonoluminescence rig.

## Slide 16
150 MK
30 MK
2.6 keV
12.9 keV
https://commons.wikimedia.org/wiki/File:Fusion_rxnrate.svg

## Slide 17
Fusion parameter continuum
Magnetic Confinement Fusion
Magnetized Target Fusion
Inertial Confinement Fusion
Linus
General Fusion
Tokamak
National Ignition Facility
Dr. Michel Laberge - Fusion Neutrons from a Strong Spherical Shock Wave Focused on a Deuterium Bubble in Water.pdf
N = 1E14 | N = 1E17 | N = 1E20 |  | N = 1E25
P = 1 Bar | P = 1 kBar | P = 1 MBar |  | P = 100 GBar
v = 0 km/s | v = 0.5 km/s | v = 5 km/sec |  | v = 370 km/s
t = 1 s | t = 1 ms | t = 7 ms |  | t = 10 ps
The Lawson criterion for sustainability of the fusion reaction (see later) depends on having the right combination of N, T and t: N = number of particles, T = temperature, t = containment time

## Slide 18
Magnetized Target Fusion or
Inertial Confinement Fusion
General Fusion

## Slide 19
General Fusion is building upon previous work and research information developed at the different National labs, and attempting to create a relatively small-scale, low-cost fusion reactor using deuterium-tritium gas, magnetic confinement, and acoustic compression.
General Fusion MTF

## Slide 20
Rotational axis
General Fusion MTF

## Slide 21
General Fusion’s reactor is a metal sphere with 220 pneumatic pistons designed to ram its surface simultaneously. The ramming creates an acoustic wave that travels through a lead-lithium liquid and eventually accelerates toward the centre [as] a shock wave.
The shock wave compresses a plasma target, called a spheromak, to trigger a fusion burst. The thermal energy is extracted with a heat exchanger and used to create steam for electricity generation.
General Fusion MTF

## Slide 22
Field-reversed configuration (FRC): a toroidal electric current is induced inside a cylindrical plasma, creating a poloidal magnetic field, reversed in respect to the direction of an externally applied magnetic field. The resultant high-beta axisymmetric compact toroid is self-confined.
Field Reversed Configuration (Spheromak)

## Slide 23
Evan Mason
Diagram of the General Fusion Reactor

## Slide 24
Inertial Confinement Fusion
First Light Fusion

## Slide 25
First Light Fusion
First Light Fusion — a spin-out from the University of Oxford — claims to be “studying the use of intense shockwaves to crush gas-filled cavities, inducing asymmetric collapses that concentrate energy in space and time.” First Light Fusion is generating huge shock fronts, that strike a bubble and cause it to collapse catastrophically, releasing energy:
http://firstlightfusion.com/
Shock wave
Bubble
Bubble
Shock wave

## Slide 26
First Light Fusion’s Scientific Advisory Board members include:
Chairman Arun Mujumdar - Professor of mechanical engineering at Stanford University and was the founding director of the US Advanced Research Projects Agency – Energy (“ARPA-E”).
Members Steven Chu - the former US Energy Secretary and 1997 Physics Nobel Prize laureate
Richard Dennis - former Director of Research and Development for Doosan Babcock Energy where he was responsible for power station boiler development and investments in new energy technologies
Richard Garwin - current IBM Fellow Emeritus at the Thomas J. Watson Research Centre in New York. At the age of 23, he was responsible for the design of the first H-bomb (1953).
Steven Rose - the former Head of Plasma Physics at Atomic Weapons Establishment Aldermaston and former Head of the Imperial College Plasma Physics Group.
First Light Fusion

## Slide 27
Inertial Confinement Fusion
National Ignition Facility

## Slide 28
National Ignition Facility uses 192 intense lasers fired onto a small (approximately 1 cm) spherical shell containing a deuterium-tritium ice mixture, exploding the outside of the shell. The rest of the shell accelerates inwards, compressing and heating the fuel for a nanosecond burst of fusion.
Inertial Confinement Fusion (laser)
Advantages:
Well advanced technology
Good control of energy release
Disadvantages:
Bad energy conversion (~1%)
Very expensive to build
Laser banks
Target

## Slide 29
Inertial Confinement Fusion

## Slide 30
Inertial Confinement Fusion
The Liquid Pendulum Engine

## Slide 31
The Liquid Pendulum
where:
f = frequency (s-1)
g = acceleration due to gravity (m/s2)
L = length of the fluid column within the pendulum (m)
f = ½p * √ ((2 * g)/L)

## Slide 32
Bearing
Eccentric rotating at the natural frequency of the pendulum
Liquid pendulum
Rotating housing
Shock chamber
The Liquid Pendulum Engine
Diagrammatic representation of one version of the Liquid Pendulum Engine

## Slide 33
Rankine combined vortex
Vf
a R
a 1/R
a
R
In normal experience, vortices tend to be found as combined vortices.
Free vortex
Forced vortex

## Slide 34
r
Shock wave front
Combined vortex within the Liquid Pendulum engine
Vf
a 1/R
R
a R
In the liquid pendulum engine, there is a discontinuity at the shock wave

## Slide 35
http://web.mit.edu/2.016/www/handouts/2005Reading4.pdf
Singularity

## Slide 36
The Liquid Pendulum Engine
Before final shock convergence, the flow has both radial and tangential components
Because the liquid pendulum engine has the shock wave between the inner and outer regions of the vortex, no viscous drag can be transmitted to the inner core. Hence a free vortex can be maintained through to the focal point (or line).

## Slide 37
The Liquid Pendulum Engine
At final convergence, all flow effectively has a radial component only
“Collinear” motion

## Slide 38
Fusion efficiency vs. temperature
Random motion => low fusion efficiency
“Collinear” motion => high fusion efficiency

## Slide 39
The natural frequency of the system is far higher than that for other implosion concepts.
The implosion process should be far more stable and efficient than that for any conceivable non-rotating system.
It is a relatively low cost system.
The coolant/liquid piston can protect the metal structure from neutron damage to a degree.
IF all the problems are resolved in terms of achieving fusion, it would be a “game changer” in terms of world energy supply.
Possible Advantages of the Liquid Pendulum

## Slide 40
Disadvantages of the Liquid Pendulum
Spinning the casing obviously increases stress within the system.
For efficient operation, the constructional materials must have good high temperature strength.
IF fusion is achieved, it’s likely that a variation of the system could be used militarily.

## Slide 41
What is the ideal scale for the system?
  Large, low angular velocity
  Small, higher angular velocity
Symmetry requirements are high for Inertial Confinement Fusion. Can they be met?
Losses:
  Friction
  Shock
Equations of state of materials at extreme temperature and pressure are not well known. CFD modelling would be problematical.
Some questions to be addressed by an R&D project

## Slide 42
There’s a strong argument that Australia should be investing strongly in projects such as this.
I’ve not been able to get any support from any Australian government agency, apart from initial support to obtain a provisional patent in 1997.
During WWII, governments funded development of:
  The jet engine
  The first digital computer (Colossus)
  Radar
  Rocketry
With climate change, we now have an equally critical need to develop radically new technology.
Conclusion

## Slide 43
Lawson Criterion

## Slide 45
Thermal velocity

## Slide 46
= 777 km/s

## Slide 47
Instability

## Slide 48
Rayleigh Taylor Instability
High density
Low density
Accelerational field
The equilibrium is unstable to any perturbations or disturbances of the interface: if a parcel of heavier fluid is displaced downward with an equal volume of lighter fluid displaced upwards, the potential energy of the configuration is lower than the initial state. Thus the disturbance will grow and lead to a further release of potential energy, as the more dense material moves down under the accelerational field, and the less dense material is further displaced upwards.
Wikipedia
Shock wave direction

## Slide 49
Heavy
Light
Richtmyer-Meshkov Instability

## Slide 50
Instability
Because of the vortex flow regime and the fact that the centrifugal field creates a near-perfect radiator surface, neither the Rayleigh-Taylor nor Richtmeyer-Meshkov instabilities should apply.
Are there other phenomena which may act to stop the singularities being achieved at the focus?
The proposed mechanism achieves only approximately spherical shock waves, and this would be non-ideal. See KTH comments later.

## Slide 51
Medium velocity compression

## Slide 52
General Fusion

## Slide 53
Rotational axis

## Slide 54
“…In this example scenario that gave near optimal fusion yield, a 2 GPa acoustic pulse is applied to the outer radius of the Pb at 1.5 m and takes 700 ms to propagate towards the plasma. At the plasma-liner interface, the pulse reaches 12 GPa and compresses the plasma in 130 ms. The plasma is 50-50 deuterium-tritium with an effective ion charge of 1.5. The plasma model includes the effects of adiabatic compression, Bremsstrahlung, Bohm thermal transport, fusion reaction chains, and fast alpha confinement. The time axis becomes more sparse around t = 0 to better show the behavior during peak compression. The plasma is compressed radially by a factor of 18, increasing the magnetic field from 5 to 1600T, the ion density from 10^22 to 6x10^25 m-3 , and the temperature from 0.1 to 15 keV. Peak fusion power is 3.6 TW and peak beta is 32%. The initial conditions for this compression scenario of Ti = 100 eV, ni = 10^22 m-3 , tE > 130 ms are within the range of achieved compact toroid (CT) conditions, the one technically challenging parameter is B0 = 5 T, which is just beyond previous results yet not unreachable…”
http://www.generalfusion.com/blog/wp-content/uploads/2016/08/Laberge-2013-Acoustically-Driven-Magnetized-Target-Fusion.pdf
General Fusion

## Slide 55
http://www.generalfusion.com/blog/category/in-the-news/this-company-could-power-the-world-for-65-billion-years/
“THIS COMPANY COULD POWER THE WORLD FOR 65 BILLION YEARS”
CNN Money features General Fusion as a future energy solution. This segment is part of a CNN Money original series Elon. Evolution which explores the challenges facing humanity today as seen by Elon Musk.

## Slide 56
A Trap to Catch the Sun

## Slide 57
Shock waves in Convergent Pipes

## Slide 58
Department of Mechanics
Royal Institute of Technology, Sweden
29th International Symposium on Shock Waves (ISSW29) July 14 to July 19, 2013
High Energy Concentration by Spherical
Converging Shocks in a Shock Tube
with Conically Shaped Test Section
N. Apazidis, M. Kjellander, and N. Tillmark

## Slide 59
1 Introduction
Converging shock waves have been extensively investigated during the past several decades. Continuing interest in this research is motivated by the ability to obtain extreme conditions in gas in the focal region. In a pioneering work, Guderley [1], (1942) published a self-similar solution of the amplification of strong converging spherical and cylindrical shock waves close to the center of convergence. Another solution to the problem was presented by Stanyukovich [2], and since then a large number of analytical and numerical studies have been conducted, see e.g. Refs. [3, 4, 5, 6, 7, 8].
When shock waves converge they accelerate as they approach the focal point. Extreme conditions are created as the shock converges at the focus. The similarity solution for converging cylindrical and spherical shocks describes a continuously accelerating shock with ever increasing temperature and pressure behind the shock front as it approaches the focal singularity. In reality, however, long before the continuum description of gas breaks down there are other obstacles that fail the idealized model. The acceleration and achievable energy concentrations seem to be mainly limited by the symmetry and stability of the shock.

## Slide 60
Perry & Kantrowitz [9] made the first experiments on converging shocks. Using a shock tube with a tear-drop inner body, plane shock waves were shaped into a cylindrical form. They found that the shock strength was amplified to such a degree that the gas emitted a sharp light flash at the instant of shock implosion. Further experiments in shock tubes following the basic principles of their design have been made by a large number of researchers, see e.g. [10, 11, 12, 13, 14, 15, 16].
Spherical shock waves focus the energy more efficiently than cylindrical shocks. Previous studies at the Department of Mechanics at KTH [12, 13, 14, 15, 16] involved creation of cylindrical shocks in a shock tube with a shock-shaping end section similar to those of Takayama et al. [10]. The aim of the present study is to create a spherical convergence process by forming plane shocks into a spherical segment and compare the results with the cylindrical studies…
N. Apazidis · M. Kjellander · N. Tillmark
Department of Mechanics, KTH, 100 44 Stockholm, Sweden

## Slide 62
The acceleration of the shock front is plotted in Fig. 2 for different initial Mach numbers. Self-similar curves are added for comparison with Guderley’s solution
r = r0(1−t/t0)a, where r is the radius and t the time.
The numerical solution agrees well with the self-similar path. At ≈ 0.5 mm from
the apex the shock has accelerated to M ≈ 25, giving a total amplification of ≈ 6.5.
Fig. 2 Shock front acceleration in the convergent section for three initial Mach numbers, MS = 1.5,3.9 and 5.5. Comparison with the spherical self-similar solution (full lines).

## Slide 63
3 Experiments
Several series of experiments were performed with argon as test gas. The propagation of the shock wave was measured for Mach numbers ranging from 1.8 to 6.0 and compared with calculations to confirm whether uniform flow with a constant velocity shock wave was formed. When the shock focuses, a bright light pulse is created in the hot gas and photometric measurements using two photomultiplier tubes connected to both optical fibers are made. A series of spectrometric measurements were made for initial Mach number and pressure MS = 3.9, p1 = 10.0 kPa, where spectra were measured at different times during the whole light pulse. Several experiments with weaker and stronger shock waves in the ranges MS = 1.5−2.4 and MS = 5.9 − 8 were also conducted.
Note temperature recorded in this method was 40,000K (see www.mech.kth.se/~nap/High_Energy.pdf)
Instabilities within the implosion shock wave and heat transfer to the metal surface probably limited temperatures beyond this.
In this context, however, it should be noted that the temperature reached is still around twice that achievable in an electric arc furnace and four times that in a furnace using chemical combustion.

## Slide 64
3.1 Spectrometric Results
3.1.1 Time-Resolved Spectrum, MS = 3.9, p1 = 10.0 kPa
Runs with p1 = 10.0 kPa and MS = 3.9 created emission of roughly 50 μs duration. The spectra from the light pulses were measured at different time instants relative to the shock implosion (Fig. 4). The spectrometer can only take one exposure per run, but the high degree of repeatability as shown by the photomultiplier records allows this method to give a reasonable accurate overview of a single event. Fig. 4 shows calibrated spectra at two instants after implosion. The spectra obtained in the beginning of the light pulse resemble blackbody radiation and fits were made to Planck’s function:
where Il is the intensity per unit wavelength l , h is Planck’s constant, c the speed of light and k Boltzmann’s constant. Least square fits to the spectra obtained from 0.25 to 7 ms after implosion show good agreement with the Planck curve. The fitted curves are plotted as dashed lines. The fits show apparent blackbody temperatures of maximum 27,000 ±1,000 K at approximately 250 ns after the maximum light intensity and about 10,000 K as the delay increases to 7 ms, see Fig. 4(b).
Due to triggering limitations the maximum intensity region has not yet been investigated spectrometrically.

## Slide 68
University of Queensland Shock Tube
Specifications
Compression tube: 229 mm ID x 26 m long
Piston mass: 92 kg
Shock tube: 76 mm ID x 10 m long
Contoured Nozzles:
  Mach 4
  Mach 6
  Mach 7
  Mach 8
  Mach 10
Nozzle supply enthalpy range: 2.5 - 15 MJ/kg
Nozzle supply pressure range: 10 - 90 MPa

## Slide 69
The energy liberated by the fusion of 1 Kg of Deuterium with 1.5 Kg of Tritium is therefore 2.82 X 10-12 X 2.99 X 1026 = 8.43 X 1014 Joules = (8.43 X 1014) / (3.6 X 1012) GWHours = 234 GWHours.
http://www.mpoweruk.com/nuclear_theory.htm
Energy output of Tritium-Deuterium Reaction
The cost of a litre of heavy water is currently about $600. Electrolysis of this would yield about 200 gm of deuterium.

## Slide 70
Sonofusion

## Slide 72
http://homepages.rpi.edu/~laheyr/Sonofusion%20Paper-pdf_Lahey_NURETH-11.pdf

## Slide 73
H.G.Wells
The World Set Free

## Slide 74
…"It has begun," he writes in the diary in which these things are recorded. "It is not for me to reach out to consequences I cannot foresee. I am a part, not a whole; I am a little instrument in the armoury of Change. If I were to burn all these papers, before a score of years had passed some other man would be doing this."
The World Set Free H.G.Wells

## Slide 75
“…The catastrophe of the atomic bombs which shook men out of cities and businesses and economic relations, shook them also out of their old established habits of thought, and out of the lightly held beliefs and prejudices that came down to them from the past.”
“The moral shock of the atomic bombs had been a profound one, and for a while the cunning side of the human animal was overpowered. Men thought twice before they sought mean advantages in the face of the unusual eagerness to realize new aspirations, and when at last the weeds revived again and "claims" began to sprout, they sprouted upon the stony soil of law-courts reformed, of laws that pointed to the future instead of the past, and under the blazing sunshine of a transforming world.”
“A new literature, a new interpretation of history, is springing into existence; a new teaching is already in the schools, a new faith in the hearts of the young. I see the crystal cup of human knowledge perpetually brimming. I see the fires of human thought rise from ten thousand altars of research, and flare out into the wilderness of space. I see the time when men will no longer be content with this little conquered planet…”
The World Set Free H.G. Wells.

## Slide 76
Nietzsche and others

## Slide 77
“...Man is a rope, tied between beast and overman - a rope over an abyss. A dangerous across, a dangerous on-the-way, a dangerous looking back, a dangerous shuddering and stopping.”
“What is great in Man is that he is a bridge and not an end: what can be loved in Man is that he is an overture and a going under…”
Thus Spake Zarathustra Nietzsche

## Slide 78
“…The Ocean lies all around you; true, it is not always roaring, and sometimes it lies there as if it were silken and golden and a gentle favourable dream. But there will be times when you will know that it is infinite and that there is nothing more terrible than infinity...”
“Alas, if homesickness for land should assail you, as if there were more freedom there - and there is no longer any 'land'!..”
Die fröhliche Wissenschaft Nietzsche

## Slide 79
“…We knew the world would not be the same. A few people laughed, a few people cried. Most people were silent.”
“I remembered the line from the Hindu scripture, the Bhagavad-Gita. Vishnu is trying to persuade the Prince that he should do his duty, and, to impress him, takes on his multi-armed form and says, 'Now I am become Death, the destroyer of worlds.' “
“I suppose we all thought that, one way or another…”
Robert Oppenheimer interviewed about the Trinity explosion, first broadcast as part of the television documentary The Decision to Drop the Bomb (1965)

## Slide 80
“…I’m not afraid, because I will ever believe in the constructive and intelligent behaviour of men – in spite of everything. Because I know the other side of the story: these pure fusion detonators that threaten us, will on the other hand give us a huge constructive engineering power that there must be no [scarcity anymore].”
“Endless energy, endless basic materials, endless forces to move huge loads, even smaller celestial bodies. We don’t have to be afraid. Paradise on earth, as it was the dream of our ancestors, is very near, if we let it happen. A free paradise based on human intelligence, based on endless energy and endless reserves of raw materials – literally endless space to discover and settle. There is enough room for all of us…”
https://monstermaschine.wordpress.com/2012/09/25/why-mankind-must-not-fear-the-pure-fusion-bomb/